## Slide 1: Robot Project Meeting – 27/09/2018
Bourgogne, Colrat, Evaux, Gaizi, Nicolle – ACE TEAM

## Slide 2: Last Meeting:
These were the points discussed:
Adding Block diagrams for each submodule and for the whole structure of the Robot Project
Using Project Management Tools for the deadlines Time Resources and such
How to set up a PI enslavement for the wheels
To be done:
@Abdoul: Show us the Office Management tools
@All Students: Create block diagrams for the submodules for each step of the Robot Project progress
@Guillaume: Add colors to the Excel PinMap cells - Done

## Slide 3: Work Planning:
Done:
  Basic Movements of the Robot with PWM signal and control of the H-Bridge through General Purpose Outputs and processing of the encoders data to calculate the distance travelled by the robot
  Obstacle detection using the Ultrasonic sensor (@Marlon: detailler)
Work in Progress
  Wheel enslavement to adjust the speed of the wheels so the robot goes straight
  Bluetooth Communication for control of the robot in non-autonomous mode and feedback for the driver of the robot
  Camera (@Maxime – mini-resumé de l‘utilite du module)

## Slide 4: Subtasks: Amine Wheel enslavment
There is a need fot wheel enslavement so the robot can adjust its speed in real time despite any external disruption (changing the floor etc)
Done:
    Configure the encoders external interrupts to destect rising and falling edges to double the resolution
    Write Acceleration and Deceleration function to control the motors inertia (Not working yet)
    Documentation on Wiki page and Code comments
To Do:
    Find the right parameters for the Proportionnal Integrate enslavement
    Implement the enslavement and test
        Deadline: Beginning of November

## Slide 5: Amine: Movements Block Diagrams
External Request Unit
GTM Timer Output Module
General Purpose Outputs
Aurix TC297
Encoder Output
PWM signal
H-Bridge*
PWM signal
Encoder Output
Port 15 pin 5
Port 10 pin 7
Port 00 pin 12
Port 33 pin 12
P00.6
EnA
EnB
P33.4
P00.4
P33.2
In2
In4
In1
In3
Motor
Motor
Out B
Out A
*H-Bridge Pin Assignment for going forward, to go backward invert In1 with In2 and In3 with In4

## Slide 6: Subtasks: Marlon, Ultrasonic Sensor
Done
  Writing in wiki
To do
  Nothing, priority shifted to other projects

## Slide 7: Marlon: Ultrasonic Sensor Block Diagrams
Ultrasonic Sensor
HC-SR04
Obstacle
TC29TF
sendTrig()
isrGetDistance()
echo
8 impulses
Trig
Echo
returnDistance()
External interrupt input
High signal for >= 10 µs
P20.9
P14.4

## Slide 8: Subtasks: Virgile, Bluetooth communication
Done:
  Read the code from the previous students
To do:
  Finish to adapt the code for our configuration
  Implement and test the bluetooth capabilities in the final code
    Deadline: Begining of november

## Slide 9: Virgile: Bluetooth communication
Bluetooth module
HC-05
Bluetooth capable device
TC29TF
rx
P14.0
P14.1
rx
tx
tx
ASCLIN
Application
serial_send()
serial_recv()

## Slide 10: Substaks: Maxime, Camera
Done
  CIF interface to control the camera
  Ethernet communication
To Do
  Send video or images to a Rasberry Pi 3B+ by Ethernet
  Run a CNN YoloV3 on the Rasberry
    Detect numbers and obstacles (send informations to the Aurix master by Bluetooth)
  Bluetooth communication (Rasberry <-> Aurix master)
  Documentation on Wiki page
Deadline: Beginning of November

## Slide 11: Maxime : Block Diagrams
Aurix TC297-Bstep
Rasberry Pi 3B+
Aurix TC297-Bstep
(master)
Camera OV7670
Eth
CIF
interface
Bluetooth
Established if :
Number is detected
Obstacle is detected

## Slide 12: Recap: Guillaume, coding on Aurix
Done:
Intern Interruption(Software),SMU
To do:
  External Interruption,SCU
  Timer Interruption