## Slide 1: Robot Project Meeting – 11/10/2018
Bourgogne, Colrat, Evaux, Gaizi, Nicolle – ACE TEAM

## Slide 2: Last Meeting:
The following are the points we discussed:
  Using the project management tool in Excel
  Doing the CNN on a raspberry pi for now
To be done:
  @All student: make block diagrams clearer by showing the link between sub-blocs, identifying the blocs within the AURIX
  @Abdoul: Forward the excel project management tool already sent to Amine

## Slide 3: Block Diagrams: Robot Project
Aurix Master
TC297B-Step
Aurix Cam
TC297B-Step
Raspberry Pi 3B+
PC command
Bluetooth
Bluetooth
Uart
Uart
Uart
Uart
Ethernet
Ultrasonic
Motors
Camera

## Slide 4: Block Diagrams: Aurix TC297-B number 1
    Movement
Equipment: 2 Motors, 2 Encoders, H Bridge
Aurix Modules: GPO, GTM TOM, ERU
Control the robot‘s movements in all 4 direction with variable speed
    Ultrasonic detection
Equipment: ultrasonic sensor HC-SR04
Aurix Modules:ERU, GPIO, STM
Detects the presence of obstacle, and measure distance to the nearest one
    Bluetooth
Equipment: Module Bluetooth HC-05
Aurix Modules: ASC(LIN)
Adds wireless communication capabilities to the robot through Bluetooth
    Camera
Equipment: camera OV7670, Raspberry Pi 3B+, 2x HC-06
Aurix Interfaces: CIF, Ethernet
Detect Numbers (from 1 to 5)

## Slide 5: Subtasks: Amine Wheel enslavment
Done:
  Trying to code Acceleration and Deceleration functions to minimize the robot‘s inertia
  Corrected a bug with PWM signal
To Do:
  Look at the Management Tools sent by Abdoul
  Find porportionate coefficient between the two motors to start implementing P correction
  Work on Integrate correction
    Deadline: Mid November

## Slide 6: Amine: Movements Block Diagrams
External Request Unit
GTM Timer Output Module
General Purpose Outputs
Aurix TC297-B Step
Encoder Output
PWM signal
H-Bridge*
PWM signal
Encoder Output
Port 15 pin 5
Port 10 pin 7
Port 00 pin 12
Port 33 pin 6
P00.6
EnA
EnB
P33.4
P00.4
P33.2
In2
In4
In1
In3
Motor
Motor
Out B
Out A
*H-Bridge Pin Assignment for going forward, to go backward invert In1 with In2 and In3 with In4
Triggers
Mesures distance and stops
Supplies Robot Motors in current

## Slide 7: Subtasks: Marlon
Done: None
To do: None

## Slide 8: Marlon: Ultrasonic Sensor Block Diagrams
Ultrasonic Sensor
HC-SR04
Obstacle
TC29TF
echo
8 impulses
Trig
Echo
External interrupt input
High signal for >= 10 µs
P20.9
P14.4
ERU
G
P
I
O
CPU ctrl
isrGetDistance()
sendTrig()
returnDistance()
P20.9
P14.4
FUNCTION OVERVIEW:
  sendTrig() : send trigger to ultrasonic sensor to start obstacle detection
  returnDistance(): check distance value for abnormal value and return it
  isrGetDistance(): interrupt routine to get distance from Echo signal
ACRONYM:
  ERU: External Request Unit
  GPIO: General Purpose Input Output

## Slide 9: Subtasks: Virgile, Bluetooth communication
Done:
  Write the Bluetooth module related section of the wiki
  Code for the Bluetooth module used in polling mode
To do:
  Finish the code for the Bluetooth module used in interrupt mode
  Implement the Bluetooth capabilities in the final code

## Slide 10: Virgile: Bluetooth communication
Bluetooth module
HC-05
Bluetooth capable device
TC29TF
rx
P15.2
P15.3
rx
tx
tx
ASCLIN
Application
serial_send()
serialRxISR()
serial_send(uint8 message):sends responses to command messages (if requested)
serialRxISR(): receives command message in interrupt mode.
commands
Responses & updates
(if requested)

## Slide 11: Substaks: Maxime, Camera
Done
  Run a CNN on the Raspberry Pi 3B+ (Detect & Indentify objects)
To Do
  Send video to a GUI (first step) and after to the Raspberry by ethernet (I asked Rahul to help me)
  Take minimum 2500 pictures to pre-train our own CNN
  Bluetooth communication (Rasberry <-> Aurix Master)
  Documentation on Wiki page (in progress)
Deadline: Mid of November

## Slide 12: Maxime : Block Diagrams
Aurix TC297-Bstep
Rasberry Pi 3B+
Aurix TC297-Bstep
(master)
Camera OV7670
Eth
CIF
interface
Bluetooth
Established if :
Number is detected

## Slide 13: Recap: Guillaume, coding on Aurix
Done:
  ERU
To do:
  Will work on the gyroscope. Due date: unknown, because still havn‘t look about that
  Will give info on acceleration, orientation