## Slide 1: Robot Project Meeting 11 – 31/01/2019
Bourgogne, Colrat, Evaux, Gaizi, Nicolle – ACE TEAM

## Slide 2: Last Meeting
These were the points discussed:
  Visit workshop to discuss about a case for the robot with the people working there - Done
  Testing the wheel’s slipping without the rubber band
  Putting the CNN with the camera on an ADAS AURIX TC39-B step
  Looking at errata sheet and look for a possible bug with the gyroscope data processing
  Bringing our own computers at Embedded World (the computers given by Infineon are using windows 7 and are slow)
  Bringing Virgile and Guillaume to visit Embedded World
To be done:
  @Alex: send us the code to enable the OCDS - Done
  @Alex: ask Gerd to give access to the AURIX conference to Guillaume - Done
  @Amine: Try taking off the rubber bands and test the slipping of the wheels - Done
  @Guillaume: Look in the errata sheets for a possible error with gyroscope data processing Gyroscope is working and integrated now
  @Abdoul & Alex & Amine: Talk about Embedded World presenting organization and go at the workshop to discuss about the robot’s case - Done

## Slide 3: Subtasks: Amine
Done
  Finish 2nd Mode with Marlon with dedicated project on GitHub
    First version is finished, the robot turns when an obstacle is detected, goes forward when the road is clear
      Problems: The ultrasonic does not see obstacles that are not at its height which causes the robot to get stuck sometimes
      Possible solution: Analyze the current consumption of the robot in real time, a current peak would mean the wheels are stuck.
  Excel sheet documenting all the cables on the robot
  Power Supply (for Servomotor) using PowerBank
To-Do
  Find a way to avoid the robot to get stuck on obtacles that are too low
    If it is stuck it should go backward and turn
          Deadline: February 7th
  Speed enslavement using gyroscope data. Takes a position in parameter, calculates the error between the current position and desired one (in orientation and position) and drives the PWMs of the two motors to reduce that error as much as possible
      Desired position information sent by the Raspberry
          Deadline: February 14th

## Slide 4: Subtasks: Maxime, Camera detection
Done
  UART communication (Raspberry <-> Aurix) – done
  Boot script for the Raspberry – done (with some bugs)
  Finish the Wiki page – done
  Consumption :
    Ptot = Prasp + Pservo = 5x[0.7 + 0.1] = 4 W x 2 = 8 W
    Cbat = 10000 mAh / 37 Wh
    Operating time = Cbat / Ptot = 4.5 hours
  See how to port the CNN on an Aurix 2G – in progress
    Deadline : 01/02/2019
Worst case

## Slide 5: Subtasks: Guillaume, gyroscope
Done :
  Data recovery done
  Issue on the processing with the madgwick filter. Euler angles have a variation of +- 5 degrees.
  Integrate the program to Amine‘s project
To do:
  Issue : Stop working at a certain time. Seems to be working without debugger. Need to check with the bluetooth recovery
    Deadline: 01/02/2019
  Wiki
    Deadline: 15/02/2019

## Slide 6: Substasks: Virgile, computer GUI
Done:
    Thread related bugs fixed
    Keyboard control of the robot
To do:
    Allow keyboard control of the robot in the GUI (not in separate console)
      DEADLINE: 08/02
    Make the python GUI into an executable application
      DEADLINE: 08/02

## Slide 7: Subtasks: Marlon – PCB
Done:
  First working algorithm for obstacle avoidance done
To do:
  PCB routing (deadline Feb. 8th)
  Find solutions to detect low obstacle (deadline Feb. 8th)